## Slide 1
NETWORK DESIGN PROJECT
College Network Project
Connecting the Data Science and Computer Science Departments
Prepared by: Aseel Alanzi Computer Science Department · University of Hail
Tool: Cisco Packet Tracer | November 2025
1

## Slide 2
OVERVIEW
Project Objective
Design and configure two interconnected departmental networks within the College of Computer Science at the University of Hail — one for the Data Science Department and another for the Computer Science Department — using Cisco Packet Tracer.
The project demonstrates core networking concepts: IP addressing, DNS configuration, static routing, and inter-network communication through routers.
2
DEPARTMENTS
2
ROUTERS
20
TOTAL DEVICES
2
DNS SERVERS
2

## Slide 3
SCOPE
Project Requirements
1
Create two separate Class C networks, one per department
2
Connect both networks using two routers with a Serial connection
3
Assign IP addresses to all router interfaces, servers, and PCs
4
Configure a DNS server in each network to resolve device names
5
Test connectivity within the same network using device names
6
Test connectivity between networks using IP addresses
7
Add clear labels and organize the topology for readability
3

## Slide 4
DESIGN
Network Design Overview
Network A
Data Science Dept.
192.168.10.0/24
Network B
Computer Science Dept.
192.168.20.0/24
Serial Link
Router-to-Router
10.10.10.0/30
Total Devices = 2 Routers + 2 Switches + 2 DNS Servers + 14 PCs (7 per department) = 20 Devices
4

## Slide 5
TOPOLOGY
Network Topology
Data Science Department — 192.168.10.0/24
Computer Science Department — 192.168.20.0/24
R0
R1
Serial 10.10.10.0/30
Switch0
Switch1
7 × PC + 1 × DNS Server
7 × PC + 1 × DNS Server
PC0–PC6 · Server0 (DNS)
192.168.10.2 – .10
PC7–PC13 · Server1 (DNS)
192.168.20.2 – .9
5

## Slide 6
CONFIGURATION
Static Routing
Each router is configured with a static route pointing to the remote department's network through the serial link.
Router0
route to 192.168.20.0/24 via 10.10.10.2
Data Science → Computer Science
Router1
route to 192.168.10.0/24 via 10.10.10.1
Computer Science → Data Science
Result: Both networks can reach each other bidirectionally through the router link.
6

## Slide 7
CONFIGURATION
DNS Configuration
Each department's server runs a DNS service, mapping every device name in its network to its IP address.
Server0 — Data Science
pc0 – pc6
192.168.10.2 – .8
server
192.168.10.10
server.datasci.local
192.168.10.10
server.datasci.local
192.168.10.10
Server1 — Computer Science
pc7 – pc13
192.168.20.2 – .8
server
192.168.20.9
server.comp-sci.local
192.168.20.9
server.comp-sci.local
192.168.20.9
7

## Slide 8
TESTING
Ping Test — Within the Same Network
From PC9, resolving and pinging device "Pc10" by name (via DNS)
C:\>nslookup Pc10
Server: [192.168.20.8] Address: 192.168.20.8
Non-authoritative answer:
Name: pc10 Address: 192.168.20.3
C:\>ping Pc10
Pinging 192.168.20.3 with 32 bytes of data:
Reply from 192.168.20.3: bytes=32 time<1ms TTL=128
Reply from 192.168.20.3: bytes=32 time<1ms TTL=128
Packets: Sent = 4, Received = 4, Lost = 0 (0% loss)
8

## Slide 9
TESTING
Ping Test — Between Different Networks
From PC0 (Data Science) to 192.168.20.2 (Computer Science) by IP address
C:\>ping 192.168.20.2
Pinging 192.168.20.2 with 32 bytes of data:
Reply from 192.168.20.2: bytes=32 time=26ms TTL=126
Reply from 192.168.20.2: bytes=32 time=42ms TTL=126
Packets: Sent = 4, Received = 4, Lost = 0 (0% loss)
TTL = 126 (vs. 128 for local traffic) confirms the packet passed through one router hop between networks.
9

## Slide 10
SUMMARY
Conclusion
✓
Two independent departmental networks were designed and fully connected
✓
Static routing enables full bidirectional communication between departments
✓
DNS resolution works correctly within each network
✓
All required ping tests passed with 0% packet loss
✓
The design reflects real-world network segmentation practices
Deliverables: Packet Tracer file (.pkt) · Project Report (.docx) · Presentation (.pptx)
10

## Slide 11
Thank You
College Network Project — CS & DS Departments
Aseel Alanzi
github.com/Aaseel11 · linkedin.com/in/aseel-alanazi410
11